## Slide 1
THE DEVELOPMENT OF ETHERNET STANDARDS: AN ANALYSIS OF IEEE 802.3 UPDATES AND INNOVATIONS
By Eun Ji Ha and Jasmine Louise Uy

## Slide 2
ABSTRACT
  Main Idea: The IEEE 802.3 Ethernet standards have driven the evolution of modern networking, supporting a range of environments from LANs to WANs.
  Purpose: This paper analyzes the major IEEE 802.3 revisions, including technical changes, rationale, and network performance impacts.
  Key Innovations: Introduces full-duplex and switched Ethernet, enhancing throughput and efficiency by overcoming traditional Ethernet limitations.
  Outcome: Illustrates how IEEE 802.3’s iterative improvements established Ethernet as a versatile, durable standard for contemporary network needs.
Keywords - Ethernet, IEEE 802.3, Local Area Network (LAN), Wide Area Network (WAN), CSMA/CD, Thick Ethernet, Thin Ethernet, Twisted Pair Ethernet, Fiber Optic Ethernet, Fast Ethernet, Gigabit Ethernet, 10-Gigabit Ethernet, Full-Duplex, Switched Ethernet, Data Transmission, Network Scalability, Network Reliability

## Slide 3
INTRODUCTION
  Ethernet’s Origin: Ethernet, developed in the 1970s, became the dominant standard for computer networking, continuously evolving to address technological advancements.
  Initial Purpose: Initially designed for local networks, Ethernet has grown to support high-speed, low-latency, and reliable connections across diverse networks, including MANs and WANs.
  IEEE 802.3 Role: The IEEE 802.3 working group played a critical role in updating Ethernet standards to improve speed, reliability, and adaptability.

## Slide 4
LITERATURE REVIEW

## Slide 5
ORIGINAL INVENTION
  Conceived in the 1970s by Robert Metcalfe at Xerox PARC for high-speed local connectivity.
  Early networks lacked scalability, struggled with data collisions, and had limited flexibility.
  Ethernet used a coaxial cable in a bus topology, enabling multiple devices to share a communication line.
  Allowed devices to check if the line was clear before transmitting, minimizing collisions.
S. Tanenbaum and D. Wetherall, Computer Networks, 5th ed., Upper Saddle River, New Jersey: Pearson, 2010.

## Slide 6
THICK ETHERNET (802.3-1985)
First standard with coaxial cabling supporting 10 Mbps, designed for industrial and office LANs.
  Unmanageable, difficult to install, and costly.
B. A. Forouzan, Data Communications and Networking, 4th ed., New York, New York: McGraw-Hill, 2007.
W. Stallings, Data and Computer Communications, 10th ed., Upper Saddle River, New Jersey: Pearson, 2014.

## Slide 7
THIN ETHERNET (802.3A)
Introduced a thinner coaxial cable for easier and less costly installation; suitable for smaller networks.
  Reduced range and ongoing susceptibility to collisions in shared media.
S. Tanenbaum and D. Wetherall, Computer Networks, 5th ed., Upper Saddle River, New Jersey: Pearson, 2010.

## Slide 8
TWISTED PAIR
  Supported 10 Mbps with UTP cables, enabling star topology with a central hub, ideal for office environments.
  Improved reliability by isolating faults, simplifying troubleshooting.
  Still half-duplex, requiring CSMA/CD for collision management.
B. A. Forouzan, Data Communications and Networking, 4th ed., New York, New York: McGraw-Hill, 2007.
W. Stallings, Data and Computer Communications, 10th ed., Upper Saddle River, New Jersey: Pearson, 2014.

## Slide 9
FIBER OPTIC
  Addressed demand for higher speed and long-distance data transmission, particularly in areas with electromagnetic interference.
  Provided high-speed connectivity over several kilometers, ideal for campus and MAN networks.
  Higher cost limited widespread use until faster networking demands emerged.
S. Tanenbaum and D. Wetherall, Computer Networks, 5th ed., Upper Saddle River, New Jersey: Pearson, 2010.

## Slide 10
SWITCHED ETHERNET
  Classic Ethernet has problems (loose connections / breaks in connections)
  start using hubs
  connect wires electrically
  easier to add and remove stations, detect breaks
  more stations = smaller share of capacity (because hubs are logically equivalent to one long cable)
A. S. Tanenbaum and D. Wetherall, Computer Networks, 5th ed., Upper Saddle River, New Jersey: Pearson, 2010.

## Slide 11
SWITCHED ETHERNET
  use switch instead
  4-48 ports, each with RJ-45 connector for twisted pair
  when station sends frame to switch port, switch can forward it using indicated Ethernet address
A. S. Tanenbaum and D. Wetherall, Computer Networks, 5th ed., Upper Saddle River, New Jersey: Pearson, 2010.

## Slide 12
SWITCHED ETHERNET
  PROMISCUOUS MODE - all frames sent to all computers
  hubs: all computer can see all traffic
  switches: traffic only forwarded to destination ports = more security
A. S. Tanenbaum and D. Wetherall, Computer Networks, 5th ed., Upper Saddle River, New Jersey: Pearson, 2010.

## Slide 13
FAST ETHERNET (802.3U)
  10 Mbps becomes 100 Mbps
  compatible with Standard Ethernet
  maintain 48-bit address, frame format, maximum and minimum frame lengths
  AUTONEGOTIATION
    devices negotiate mode or data rate
B. A. Forouzan, Data Communications and Networking, 4th ed., New York, New York: McGraw-Hill, 2007.

## Slide 14
FAST ETHERNET (802.3U)
  100Base-TX - 2 pairs of STP or category 5 UTP
  100Base-FX - 2 pairs of fiber optic
  100Base-T4 - 4 pairs of category 3 or higher UTP
B. A. Forouzan, Data Communications and Networking, 4th ed., New York, New York: McGraw-Hill, 2007.

## Slide 15
GIGABIT ETHERNET (802.3Z)
  data rate now 1000 Mbps
  compatible with Standard and Fast Ethernet
  maintains 48-bit address, frame formatting, min and max frame length
  supports autonegotiation
  allows point-to-point links via switches and broadcast channels via hubs
B. A. Forouzan, Data Communications and Networking, 4th ed., New York, New York: McGraw-Hill, 2007.
J. F. Kurose and K. W. Ross, Computer Networking: A Top-Down Approach, 7th ed., Hoboken, New Jersey: Pearson, 2017.

## Slide 16
GIGABIT ETHERNET (802.3Z)
  CARRIER EXTENSION
    min frame length now 512 bytes (8x longer)
    padding for shorter frames
B. A. Forouzan, Data Communications and Networking, 4th ed., New York, New York: McGraw-Hill, 2007.

## Slide 17
GIGABIT ETHERNET (802.3Z)
  FRAME BURSTING
    carrier extension is inefficient when sending multiple short frames (data is redundant)
    send multiple frames connected together using padding
    keeps the channel from being idle
    as if one big frame is being sent
B. A. Forouzan, Data Communications and Networking, 4th ed., New York, New York: McGraw-Hill, 2007.

## Slide 18
GIGABIT ETHERNET (802.3Z)
  1000Base-SX - 2 wires of short-wave fiber optic
  1000Base-LX - 2 wires of long-wave fiber optic
  1000Base-CX - 2 wires of STP
  1000Base-T - 4 wires of category 5 UTP
B. A. Forouzan, Data Communications and Networking, 4th ed., New York, New York: McGraw-Hill, 2007.

## Slide 19
  improvement on switched ethernet
  instead of half-duplex (can only either send or receive)
  two links (one for sending, one for receiving)
  no need for carrier sensing and collision detection
B. A. Forouzan, Data Communications and Networking, 4th ed., New York, New York: McGraw-Hill, 2007.
FULL-DUPLEX SWITCHED ETHERNET

## Slide 20
  collisions happen in half-duplex
  need Carrier Sense Multiple Access with Collision Detection (CSMA/CD) protocol
  carrier sense = wait until channel is empty before transmitting
  multiple access = interfaces have equal priority
  collision detection = if there’s a collision, stop transmitting and restart after a random time
A. S. Tanenbaum and D. Wetherall, Computer Networks, 5th ed., Upper Saddle River, New Jersey: Pearson, 2010.
C. E. Spurgeon, Ethernet: The Definitive Guide, 1st ed., M. Stone and C. Toporek, Eds., O'Reilly & Associates, 2000.
FULL-DUPLEX SWITCHED ETHERNET

## Slide 21
  speed up -> 10 Gbps
  maintains 48-bit address, frame format, min and max frame lengths
  compatible with Standard, Fast, Gigabit Ethernet
B. A. Forouzan, Data Communications and Networking, 4th ed., New York, New York: McGraw-Hill, 2007.
TEN-GIGABIT ETHERNET

## Slide 22
  allows connection of existing LANs into a MAN or WAN
  only operates in full duplex mode, no CSMA/CD
B. A. Forouzan, Data Communications and Networking, 4th ed., New York, New York: McGraw-Hill, 2007.
TEN-GIGABIT ETHERNET

## Slide 23
METHODOLOGY
Compared ChatGPT insights on Ethernet standards with the Literature Review (RRL).
Process:
  Information Gathering: ChatGPT was queried on key Ethernet standards (e.g., Thick, Thin, Twisted Pair, Fiber Optic, Fast, Gigabit, Ten-Gigabit Ethernet).
  Verification: Compared responses with RRL data to confirm accuracy.
Key Findings:
  Consistent Information: Confirmed details on standards like Thick Ethernet (10 Mbps, coaxial), Thin Ethernet (easier installation), Fiber Optic Ethernet (long-distance, EMI-resistant), and Fast Ethernet (100 Mbps, UTP/fiber).
  Additional Insights from ChatGPT: Applications for Fast, Gigabit, and Ten-Gigabit Ethernet.
Evaluation:
  Advantage: ChatGPT provided accurate, supplementary insights.
  Limitation: Lack of source citations limits verification.

## Slide 24
CONCLUSION
  many updates since creation
  to improve performance or fix issues
    faster speeds
    address collisions
    change in cabling
    convenience (thick to thin, classic to switched)
  stay compatible with older standards

## Slide 25
CONCLUSION
  ChatGPT gives same information as RRL
  also gives some additional information
  no sources so cannot be verified

## Slide 26
REFERENCES
A. S. Tanenbaum and D. Wetherall, Computer Networks, 5th ed., Upper Saddle River, New Jersey: Pearson, 2010.
B. A. Forouzan, Data Communications and Networking, 4th ed., New York, New York: McGraw-Hill, 2007.
W. Stallings, Data and Computer Communications, 10th ed., Upper Saddle River, New Jersey: Pearson, 2014.
J. F. Kurose and K. W. Ross, Computer Networking: A Top-Down Approach, 7th ed., Hoboken, New Jersey: Pearson, 2017.
C. E. Spurgeon, Ethernet: The Definitive Guide, 1st ed., M. Stone and C. Toporek, Eds., O'Reilly & Associates, 2000.

## Slide 27
THANK YOU